OSPAR workshop on the environmental impact of placement of carbon dioxide in geological structures in the maritime area

Trondheim, 26-27 October 2004

Context: One option to combat climate change and ocean acidification, need for complementary measures.

What is geological storage?

- Storage in geological structures such as depleted oil- and gas reservoirs, deep saline aquifers and unminable coalmines. Must be distinguished from ocean storage.

- There is a potential of geological storage areas in the OSPAR maritime area.

- It is technically feasible: We have experience from ongoing storage-projects both onshore and offshore in Europe and elsewhere, such as the Sleipner project, Weyburn, the Netherlands, Algeria.

- Several storage projects are in the pipe-line both in Europe (e.g. Germany, Austria) and elsewhere (Australia).

How safely can CO2 be stored?

- Many of these structures have contained oil and gas for tens to hundreds of millions of years.

- Potential storage sites have to be examined and selected carefully to minimize risks of leakage through risk assessments.

- Storage sites are different, and technical and operational solutions have to be adjusted to each storage site. Best engineering practice should be employed.

- Studies of natural analogues are useful. The state of the art methods used in geological surveys and petroleum exploration can be used to predict performance of a storage site.

- The development of guidelines for risk assessment would be useful.

What are the effects of CO2 on the marine environment?

- Risk of leakage has to be evaluated against the effects of atmospheric CO2 on the marine environment.

- Oceans play an important role in the global climate system. There are important feedback effects between changes in the oceans and changes in the global climate.

- We already know a lot about the chemical effects of CO2 on the marine environment, as a large proportion of atmospheric CO2 is absorbed into the oceans and reduces seawater pH.

- Climate change has profound impacts on the productivity, biodiversity and sustainability of the marine ecosystems.

- Increased CO2 – decreased pH. Even small changes in the pH-values in the oceans, have large impacts on marine ecosystems (incl possibly on cold water coral reefs).

How can injected CO2 be monitored?

- Why monitor?

  - Detect distribution and displacement of CO2, which may have environmental consequences (effects on humans, animals, the environment)

  - Ensure performance/economics (keep CO2 separated from the atmosphere – may be important for emissions accounting)

- Various methods are available and established technology can be used. Geophysical and geochemical methods are both useful.

- Also, new and improved methods will be developed.

- Experience from several projects (Sleipner in the OSPAR maritime area), including the studies of natural analogues, give valuable information.

- Potential leakage tends to be from isolated spots – faults/fractures and wells.